## Slide 1
Transfer of a miniaturized method for
high-throughput screening of biomass
pretreatment and saccharification and application
on poplar and miscanthus clones
Nassim Belmokhtara,b, Vincent Seguraa, Brigitte Chabbertc, Nathalie Boizota,b, Kévin Adera,b, Stéphanie Arnoultd, Maryse Brancourt-Hulmele, Jean-Charles Bastiena, Catherine Bastiena, Jean Paul Charpentiera,b
a INRA, Centre Val de Loire, UR 0588 AGPF, 45075 Orléans Cedex 2 , France
bINRA, Centre Val de Loire, Plateforme Régionale GénoBois, 45075 Orléans Cedex 2, France
cINRA, Centre Nord Picardie Champagne, UMR 0614 FARE, 51100 Reims, France
dINRA, Centre Nord Picardie Champagne, UE GCIE, Estrée-Mons, 80203 Péronne, France
eINRA, Centre Nord Picardie Champagne, UR AgroImpact, Estrée-Mons, 80203 Péronne, France
Introduction
In order to meet increasing demand for second-generation biofuels, exploring large sets of lignocellulosic biomasses appears to be one of the key levers to improve bio refinery yields.
Poplar and miscanthus breeding programs have provided large sets of varietal outputs, whose saccharification potential assessment could lead to identify the best biofuel-oriented varieties.
2nd generation bioethanol production
Assessment of saccharification potential
High saccharification yielded varieties
Plant breeding programs
3
2
1
Objectives of this study:
1- Transfer into breeding programs and adaptation of a high-throughput screening method developed at NREL (USA)1
2- Demonstration, on poplar and miscanthus biomass, of the importance of pretreatment step in screening process
Experiments
HPLC
GOPOD assay (Megazyme®)
Glucose quantification
Biomass preparation
Pretreatment
Enzymatic hydrolysis
Enzymatic hydrolysis
(50° C, 70 mg.g-1 Dry Matter of Cellic Ctec-2)
Enzymatic hydrolysis without pretreatment
Steam generator
Cellkraft®
Stainless pretreatment reactor
PARR Instrument®
Steam (180° C)
Lignocellulosic biomass from short rotation coppice (SRC) and very short rotation coppice (vSRC) poplars and miscanthus clones
Fully automated station for biomass grinding (A) and precise dispensing (B)
(Xyloforest project)
Hastelloy 96-well microplate (SBS-type):
Thermal and corrosion resistance
4 steam ports surrounding each well
Stackable in Hastelloy holder
5 mg of biomass per well (1,67 % w/v)
Reaction volume: 340 µL per well
(NREL, Denver, USA)
Results
Based on the comparison of the sugar release of poplar and miscanthus biomasses, our approach allowed us to stress the importance of a pretreatment step before enzymatic hydrolysis to magnify the expression of the genetic variability. Furthermore, this approach revealed different responses to saccharification of SRC and vSRC poplar biomasses without or after a pretreatment.
Our developed high-throughput method is well adapted to screen, with high accuracy, a large set of samples from different lignocellulosic biomasses to evaluate their potential for saccharification.
Chart: 
| UT | PT
Box 1 - hidden | 0.28019 | 0.50706
Box 2 - lower | 0.069334 | 0.28908
box 3 - upper | 0.086605 | 0.070504
Chart: 
| UT | PT
Box 1 - hidden | 0.20031 | 0.62124
Box 2 - lower | 0.0097246 | 0.035446
box 3 - upper | 0.016479 | 0.070362
Poplar (20 samples)
Miscanthus (15 samples)
1- Impact of pretreatment on the variability of glucose release percentage
2- High-throughput screening of 10 SRC and 10 vSRC poplar varieties
Hot water pretreatment in 96-well microplates increases significantly saccharification yield for both plants
More variability in glucose release is observed after hot water pretreatment mainly for poplar clones
vSRC poplars release higher glucose amounts than SRC ones when saccharified without pretreatment (A)
SRC and vSRC poplars show similar enzymatic glucose yield after hot water pretreatment (B)
More variability in glucose release is observed for SRC poplar without pretreatment (A) in contrast to vSRC ones which express more variability after hot pretreatment (B)
Conclusions
A
B
Reference:
[1] M.J. Selig, M.P. Tucker, R.W. Sykes, K.L. Reichel, R. Brunecky, M.E. Himmel, M.F. Davis and S. R. Decker. Lignocellulose recalcitrance screening by integrated high-throughput hydrothermal pretreatment and enzymatic saccharification. Industrial Biotechnology 6 (2010), 104-111.
Acknowledgments:
This work was funded by BPIFrance in the R&D project Futurol
Innovative equipments was funded by Xyloforest, an Equipex Project (ANR) (INRA Aquitaine)
E-mail contacts :
Nassim.Belmokhtar@orleans.inra.fr
Jean-Paul.Charpentier@orleans.inra.fr
B
A
Untreated
Pretreated
Untreated
Pretreated