## Slide 1
Harvesting slash residues in forests: a sustainable opportunity for the bioenergy sector?
Saint-André L, Achat D., Bilot N., Augusto L., Legout A., Wernsdörfer H., Laclau J-P., Deleuze C., Ranger J.
Session on Biomass for Energy

## Slide 2
Context and main issues Energy policies
Current energy policies are characterized by two complimentary objectives:
to reduce fossil energy consumption
to develop renewable energies market, particularly woodfuel sector
European energy policies target a proportion of 20% renewable energies in total energy consumption of whole EU for 2020 (2009/28/CE) - France: 23%
Increase forest management intensity
Sto very short rotation cropping systems dedicated to wood production (see Marron et al. this session)
Increased harvesting in existing forest ecosystems (this presentation)
Impact on soil and forest sustainability?

## Slide 3
Context and main issues Scientific challenges
Soil fertility in forest ecosystems ?
Total reserves = long term
Soil organic matter
Soil mineral
Weathering = current restoration
Mineralization = current restoration
Exch. + available reserves = current
Uptake from the trees
Restitution by litter falls
and root turn-over
Soil chemical fertility is based on a small amount of nutrient circulating rapidly in the ecosystem
BIOCHEMICAL Sub-Cycle
- translocations
BIOLOGICAL Sub-Cycle
- Canopy Exchanges
- Nutrient uptake
- Immobilization
- Litter falls
- Mineralization of organic matters
GEOCHEMICAL Sub-Cycle
- Atmospheric deposits
- Weathering
- Drainage
- Run-off
The partitionning between these sub-cycles is ecosystem-dependant
Hanson et al. 2015

## Slide 4
Context and main issues Scientific challenges
Harvesting slash residues = modification of the biological cycle
Organic matter mineralisation (C, N, Cations)
Contribute to the maintenance of soil chemical properties and soil biodiversity (macro-, meso-, micro- fauna)
Beech, 80 years, Fougères, France
192
65
3
74
205
275
2
6.5
5
80
113
20
22.5
56
Eucalyptus, 6 years, Pointe-Noire, Congo
Douglas fir, 60 years, Vauxrenard, France
352
45
50
16
195
154
121
225
From, Laclau, 2001; Nys 2007; Ranger 2004

## Slide 5
A concrete example, the CIFOR network
Assessing the Impact of Slash Management on the Eucalyptus Productivity
6 countries, 10 sites
Eucalyptus plantations
Same treatments applied in each country (bare soil to double slash)
Unique modelling framework to assess the impact of slash management on the site index (SI), the ability of trees to produce biomass at a given SI, the between tree competition and the height/diameter growth partitioning
Nambiar et al. 2008

## Slide 6
A concrete example, the CIFOR network
Assessing the Impact of Slash Management on the Eucalyptus Productivity
Dominant height as a function of age
Site Index
- Unchanged
- Temporary changed
- Changed
Saint-André et al. 2008

## Slide 7
A concrete example, the CIFOR network
Assessing the Impact of Slash Management on the Eucalyptus Productivity
Stand Basal Area Growth as function of dominant height growth
Capacity of trees to produce biomass at a given Site Index
- Unchanged
- Changed but non significantly
- Significantly Changed
Saint-André et al. 2008

## Slide 8
A concrete example, the CIFOR network
Assessing the Impact of Slash Management on the Eucalyptus Productivity
Saint-André et al. 2008
As a result the impact reached up to 30% for height growth, 20% for the circumference and 70% for the stand basal area after one rotation
Impact correlated to a loading index (N in residues/ [N] in soil)

## Slide 9
Generalisation, meta-analysis from different networks in the world
Achat et al. 2015
Mainly:
- ‘‘North American long-term soil productivity’’ study (LTSP network)
- Experiment network in Scandinavia
- ‘‘Site Management and Productivity in Tropical Plantation Forests’’ network (CIFOR project)
43% in North America (29% in USA, 14% in Canada)
45% in Europe (35% from Scandinavia)
Consequences on nutrient outputs (data compilation from 230 articles, 749 case studies)
Consequences on soil properties and tree growth (data compilation from 140 articles, 168 case studies)

## Slide 10
Main harvest treatments considered in the meta-analysis.
Conventional stem-only harvest (S(WB), control) compared to different types of intensive removals or to stem wood harvest (S(W), stem bark left on site; mitigation measure).
Generalisation, meta-analysis from different networks in the world
Achat et al. 2015

## Slide 11
Generalisation, meta-analysis from different networks in the world
Achat et al. 2015
Increases in nutrient exportation (% changes)
Nutrient exportation as % of nutrient socks in soils (0-80 cm)
Examples for: Treatment S(WB)B vs S(WB): hatched boxplots
Treatment S(WB)BF vs S(WB): solid boxplots

## Slide 12
Generalisation, meta-analysis from different networks in the world
Achat et al. 2015
Increases in nutrient exportation (% changes): relationships with stand age
S(WB)BF
Open circle, broadleaf trees; grey square, sparse canopy coniferous (mainly Pinus, also Larix or Agathis); black triangle, dense canopy coniferous (Picea, Abies and Pseudotsuga).
S(WB)

## Slide 13
Generalisation, meta-analysis from different networks in the world
Achat et al. 2015
mean changes for S(WB)BF vs S(WB
-40 % in wood debris, -10% in forest floor and deep soils
-6 to -12% in total N, P, Ca;
-8 to -17% available soil P and CEC, S/T
-0.2% in soil pH
-8% in microbial activity; -23 to -37% in enzymatic activity
-27% in net N mineralization fluxes
-3 to -7% in tree growth

## Slide 14
Toward an optimized chain for the sustainable use of forest biomass for energy
Bilot 2015
Soil fertility, soil biodiversity
Sustainability
Energy produced
Energetic issue
Energy used to harvest trees
Nutrient Exportations

## Slide 15
Toward an optimized chain for the sustainable use of forest biomass for energy
Modified from Bilot 2015
Tree and stand growth
Harvesting decisions (management- and/or demand- driven)
Machine used – Men/month – Fuel – etc…
Biomass, nutrient content in the different compartments
Energetic caracterisation of the exported material
Nutrient exportation
Energy used during the process
Energy used during the harvest
Exported Biomass and Nutrient content; Humidity
Energy produced (ex by pellets)
HHV
Ash content
CAPSIS
ForEnerChips
Impact on soil fertility, soil biodiversity
Remediation by ashes
Ashes production
Critical point 1 : Site effect on nutrient concentration in the tree compartments
Critical point 2 : Knowledge on the energy used in a given harvesting operation
Critical point 3 : Conversion matrix to assess PCI and Ash content
Critical point 4 : Indicators on the impact, responses curves
Critical point 5 : Non desirable elements in ashes, impact on ecosystem functionning

## Slide 16
Toward an optimized chain for the sustainable use of forest biomass for energy
Critical point 1 : Site effect on nutrient concentration in the tree compartments
Wernsdörfer et al. 2014
Conc. Wood
Conc. Bark
Conc. Tot
(Wood + Bark)
Size of the compartment
Site effect on the curve – not directly related to soil concentrations
M-POETE, A Mobile-Platform for the Observation and the Experimentation in Terrestrial Ecosystems (Zeller et al)
Infra-red spectrometry in situ
Translation of the curves (site effect) by making few measurements on the field

## Slide 17
Toward an optimized chain for the sustainable use of forest biomass for energy
Critical point 2 : Knowledge on the energy used in a given harvesting operation
Bilot 2015
Simulation of different scenarios at each step from the forest to the mill

## Slide 18
Toward an optimized chain for the sustainable use of forest biomass for energy
Critical point 3 : Conversion matrix to assess HHV and Ash content
Wood energy production chain
Ecology, Biogeochemistry
Energy
C
N S P K Ca Mg Mn Na Al
C, H, O, N
"Dry material": 65°C
"Dry material": 103°C
Heating value, Ashes
Bilot et al.
Bilot et al. 2015

## Slide 19
Toward an optimized chain for the sustainable use of forest biomass for energy
Critical point 4 : Indicators on the impact of increased harvest on tree growth, responses curves
Critical point 5 : Non desirable elements (such as heavy metals) in ashes, impact on ecosystem functioning
Two projects have started in 2014, funded by the French environmental and energy management agency (ADEME)
INSENSE: Ecosystems sensitivity indicators to increased biomass removal in forests
RESPIRE: Slash management in forests: potentialities, environmental impact and compensation by wood ashes.
Starting points for a future collaboration ?