## Slide 1
Eric Ceschia (INRAE) & Ahmad Al Bitar (CNRS)
A. Ihasusta, G. Pique, T. Wijmer, R. Fieuzal, L. Arnaud (CESBIO), E. De Laroche (ASP), A. Tarko & D. Laurent (IGN)
CNRS, CNES, INRAE, IRD, Univ. Toulouse III
Remote sensing & modelling to assess cropland
C budget components (on mineral soils)
Joint EUSO-ORCaSa meeting
ISPRA, 26/10/2022

## Slide 2
  Questioning of the durability of conventional agriculture  food security, resilience, climatic & other environmental impacts)
Context/Societal challenges
Illustrations: Arbre et Paysage 32
Agro-ecological practices
  Lack of large scale tools to quantify cropland C budgets and its components (e.g. biomass, CO2 fluxes) at plot level and to analyse the effect of management practices on C budgets
C storage
 4p1000 initiative
No till
Cover crops
Agroforestery
Joint EUSO-ORCaSa meeting, Ispra, 26th October 2022
Need for methods & tools adapted to different context (CAP, C market) combining crop modelling and high resolution remote sensing  e.g. H2020 NIVA & ORCaSa & ClieNfarm, Soil Carbon Farming (Climate Kic) projects

## Slide 3
Why is it possible now ?
Clear or cloudy sky conditions
Rugosity & surface water content
Sentinel 1
(10 m, 6j, Radar)
Sentinel 2
(10 m, 5j, Optical)
Clear sky conditions
Reflectances (13 bands)
Land cover
LAI/
phenology
Albedo
2%
40%
Soil water content
Biomass
Soil work
Monitored
parameters
Dynamic mapping
How to use those data to quantify C budget and its components ?
Sentinel
A
Revolution !!!
(free all over
the globe)
!! Monitoring of superficial Soil Organic C content do not provide information on SOC stock changes !!
Notes: A la différence des anciennes missions spatiales…les nouveaux satellites S1&2 lancés en 2015 n’obligent pas à faire un compromis entre résol spatiale et temporelle

## Slide 4
  A similar conceptual approach: Carbon budget (Smith et al 2010)
Indicators are calculated for each cropping year (at 10m/plot level), but can be summed over several years (crop rotation),
Methodology:
  Calculations of TIER 1 (CO2 fluxes) and TIER 2 (C budget) are based on empirical approaches and can be applied to most crops species except rice,
  TIER 3 is based on the SAFYE-CO2 crop model calibrated with satellite observations (LAI from Sentinel 2)  allows other indicators to be calculated (biomass, yield, CO2 fluxes, evap/transp…), but only parametrised yet for few crop types species (straw cereals, sunflower, maize and rapeseed) + cover crops.
  C budget = Net CO2 flux – C harvested + Org. manure
TIER 1
TIERs
2 & 3
Carbon budgets indicators
Farmer’s data (FMIS)

## Slide 5: Carbon indicator Tier 1 : principle
Empirical approach  most crop species except rice
Based on Ceschia et al. (2010)
Vegetation soil coverage (days)
Net annual CO2 flux depends on the total number of days with active vegetation covering the soil ƒ(NDVI, solar radiation)
IACS data (LPIS + GSAA)
Cropland sites flux tower
Days with active vegetation
Net annual CO2 flux
Open source code https://gitlab.com/nivaeu/uc1b_indicators_tool
Under validation with post 2016 ICOS data
- Days with low radiation
Vegetation index (NDVI)
Solar radiation (ERA5)
+ uncertainties

## Slide 6
Carbon Tier 1 : National scale 10m resolution
NIVA’S algorithm + Iota2 software
With the support of
Associated uncertainty map coming soon

## Slide 7
Carbon Tier 1 : National scale 10m resolution
Crop Comparison of the Net Annual CO2 fluxes (NEP)
In general winter crops fix more CO2 (longer vegetation cycle) but :
- Overestimated here for winter crops  low radiation effect not accounted for here
- Maize fix a lot of CO2 in Bertagne
Joint EUSO-ORCaSa meeting, Ispra, 26th October 2022

## Slide 8
Carbon Tier 1 : National scale 10m resolution
Net Annual CO2 fluxes (NEP) for maize on France in 2019
Maize types (LPIS data)
Grain maize
Silage maize
Cover crops before silage maize
Cover crops on 50% of the grain maize
No cover crop before grain maize
Pointe de l’Alsace
tC of CO2/ha

## Slide 9: Carbon indicator Tier 2 : principle
Empirical approach  most crop species except rice
Tool availlable at: https://gitlab.com/nivaeu/uc1b_indicators_tool
Currently tested in France with
For our calculations main limitations is access to reliable farmer’s data
But once the TIER1 is produced with our tools, farmers, cooperatives, Paying agencies, agrifood companies…can produce TIER2 themselves
Farmer’s data
Assesses Soil Organic Carbon stock changes
Joint EUSO-ORCaSa meeting, Ispra, 26th October 2022

## Slide 10: Carbon indicator Tier 3 : principle
Modelling approach  wheat, maize, sunflower, cover crops
CO2 flux are calculated by the model that is calibrated by Leaf Area Index derived from the Sentinel-2 data, farmer’s data are used to finalise the C budget calculation
Pique et al. (2020 a & b)
+ yield, biomass, CO2 fluxes
LAI
IACS
Large set of validation data: e.g. from ICOS flux tower network, Spatial Regional Observatory…
https://framagit.org/ahmad.albitar/safye_co2.git

## Slide 11: Plot scale regional estimates for Sunflower
Plot scale simulations  Analysis of spatio -temporal variability of the components of the carbon budget
Pique et al (2020b) in Remote Sensing
Net CO2 flux C harvested C budget
Effect of summer cover crops/weeds on the C budget components  only satellite based approach allows to account for that
Joint EUSO-ORCaSa meeting, Ispra, 26th October 2022

## Slide 12: The AgriCarbon-EO processing chain
A scalable solution for large scale/high resolution cropland carbon budget monitoring compliant with recommendations by the CIRCASA initiative (Smith et al. 2020) and the voluntary C market standards
Soil model (AMG) (4)
Clivot et al. (2019) (4)
PhD
PhD
An end to end processing chain adapted to large scale/high resolution (10m) applications: parallelized bayesian inversion approach  uncertainty analysis, super computers…(Wijmer et al. submitted)
Sentinel 2
ERA5
Soilgrids
Activity data
Straw management
Organic amendments
Crop residues + uncertainty
LAI
+ uncertainty

## Slide 13: High resolution C budget components with AgriCarbon-EO
Net annual CO2 fluxes for 2018 straw cereals in South West France (10 m resolution)  4h of computing
10m resolution C budget map for cover crop/maize/wheat crop rotations (Villeneuve farm, France )
Whole Sentinel 2 Tile (31TCJ)
Cover crop biomass Uncertainty map
gC/m2
Net annual CO2 flux (gC-CO2/m2/yr)
g DM/m2
CO2 fixation / soil C storage
CO2 losses / soil C losses
Collab. with the Nataïs company (Naturellement popcorn project)  farmers get a bonus according to the C they store in the soil with cover crops
+ farmer’s data

## Slide 14
Conclusions
Based on (mainly) open data & tools, C indicators were produced with 3 levels of complexity at pixel/plot scale over large territories but with a similar conceptual approach (i.e. C budget);
TIER 1: easy to implement at large scale/high resolution but does not account for some of the farmer’s practices which may impact the results (e.g. organic amendments),
TIER 3 (model) also require farmer’s data, offer higher levels of accuracy and provides additional useful indicators (yield, biomass, water requirements) but are less operational as for each new crop specie the model needs to be parametrised/validated  transposability currently tested (NIVA, ClieNfarm projects),
TIER 2: more accurate, technically easy to implement  the main limitation is the access to reliable farmer’s data (next is to use API’s to connect to the FMIS),
Solutions exist for large scale/high resolution monitoring of C budget components but access to reliable data on farmer’s practices is the main limiting factor
Possibility to combine different TIER approaches (ex. TIER2 and 3) when relevant : CAP, NDCs
CAP, NDCs
CAP, NDCs,
C market
Joint EUSO-ORCaSa meeting, Ispra, 26th October 2022

## Slide 15: Thanks for your attention and thanks to our financers
If you want to have more details concerning our work:
- visit: https://www.cesbio.cnrs.fr/agricarboneo/
contact us at : eric.ceschia@inrae.fr & ahmad.albitar@gmx.com
ORCaSa
Naturellement
popcorn

## Slide 16
Overview of the Agricarbon-EO processing chain
Downloads, colocates and regrids data from optical satellites (Theia* ), weather reanalysis ERA5LAND (ECMWF**)/SAFRAN & validation data
Bayesian LUT based Inversion of Prosail for each image to obtain LAI +uncertainties
Bayesian LUT based assimilation of LAI time series into SAFYE-CO2 to obtain parameters and variables
Produces
Quality indicators & uncertainties
Maps of variable & parameter as well as their distributions.
SAFYE-CO2 simulation
over one Sentinel2 tile 4h
https://www.cesbio.cnrs.fr/agricarboneo/
spatial
temporal
Notes: 1 min

## Slide 17
Copernicus HR LAI product
29 Juin 2006
Spot, Landsat,
Sentinel 2
Yield
SAFY-CO2
(Pique et al. 2020a et b)
Biomass & yield data
Modelling approach with SAFYE-CO2
Crop param
Flux tower network
Rg,T°C
Leaf Area Index
Crop
Maps (LPIS)
Climatic data (e.g. ERA-5)
Calibration of phenological parameters & light-use efficiency parameter
Biomass,
Yield
Farmer’s data (FMIS)
Few farmer’s data needed to calculate C budget
C budget for wheat gC.m-2)
C budgets
CO2 fluxes

## Slide 18: Carbon indicator Tier 2 : principle
+ Farmer’s data
Tested in South West France with the collaboration of
Tool availlable at: https://gitlab.com/nivaeu/uc1b_indicators_tool
C budget (tC/ha)
NEP (tC of CO2/ha)
Net annual CO2 flux map
Annual C budget map

## Slide 19: Overview of AgriCarbon-EO